# Decorative Concrete Sealer

# Company Details

South Coast Decorative Concrete Supplies Pty Ltd

1 McIntyre Way, Bomaderry, NSW 2541, Australia

Tel: (02) 44235111	Fax: (02) 44235105

Emergency Telephone: 000

### Product Information

This Product is classified as hazardous according to criteria of Worksafe Australia

| Product Names: | Decorative Concrete Sealer |
| --- | --- |
| Other Names: | Concrete Resurfacing, High Gloss, Prime and Seal, Economy, Colour-Seal and Decorative Concrete Sealer 28. |
| Shipping Name: | Resin Solution, Flammable |
| U.N. Number: | 1866 |
| D.G. Class: | 3 |
| Subsidiary Risk: | N/A |
| Hazchem Code: | 3[Y] |
| Packaging Group: | III |
| Poisons Schedule: | 5 |
| Chemical Description: | Pigmented/unpigmented solution of acrylic copolymer resins & hydrocarbon solvents |
| Use: | Clear & pigmented |
| Physical Description / Properties |
| Appearance: | Clear or pigmented viscous liquid |
| Odour: | Hydrocarbon solvent |
| Boiling Point (°C): | Range 137-175 |
| pH: | N/A |
| Relative Density: | 0.922 |
| Shelf Life: | 18 months |
| Other Properties |  |
| Flammability Limits: | See ‘Fire/Explosion Hazard’ under ‘Safe Handling Information’ |
| Solubility in Water: | Negligible |
| Solubility in Organic Solvents: | Soluble |
| Vapour Pressure (kPa): | 1.7 |
| Volatiles %: | 73 |
| Flash Point (°C): | 43 |

| Ingredients |  |  |
| --- | --- | --- |
| Chemical Entity | C.A.S. Number | Proportions % |
| Liquid Hydrocarbons | 1330-20-7 / 64742-95-6 | > 60 |
| Acrylate/Methacrylate Copolymer | 28262-63-7 | 20-30 |
| Plasticizer | N/A | < 5 |
| Clay Filler | N/A | < 5 |

Health Hazard Information

Health Effects

Effects of overexposure – Acute

High vapour concentrations are irritating to the eyes and respiratory  tract, may cause headaches and dizziness, are anesthetic and may have other central nervous system effects.

Effects of Exposure – Chronic

Prolonged or repeated contact with the skin may irritate and cause dermatitis.

##### Emergency and First Aid Procedures

###### Swallowed

Do not induce Vomiting. Give a glass of water and seek immediate medical attention.

###### Eye

Immediately hold open eyes and flush with water continuously for at least fifteen minutes. Seek medical attention.

###### Skin

Remove contaminated clothing and wash affected area with plenty of soap and water

###### Inhaled

Remove to fresh air and apply artificial respiration if not breathing. Keep person calm and seek medical attention.

###### Advice to Doctor

Treat symptomatically

###### Precautions for Use

Exposure Standards

50 ppm for 8 hour working day exposure

Engineering controls

Avoid heating product

Ventilation

Use in well ventilated area or use local exhaust – face velocity > 20 m/min

Personal Protection

| Gloves: | Long impervious PVC |
| --- | --- |
| Overalls: | Cotton |
| Eyes: | Chemical goggles resistant to aromatic hydrocarbon solvents |
| Respiratory: | Brush or Roller Application: Type !, Class 1 organic vapour (to AS1715) (eg 3M Easicare 5101/5201/5301, Type 1A) Spray Application: Above in conjunction with Class P1 particle filter |
| Other: | Practice strict hygiene – wash before breaks and after finishing |

Flammability

Flammable liquid

Safe Handling Information

Storage and Transport

Store away from heat, alkalis, foodstuffs and empty foodstuff containers and oxidising agents (such as chlorates, nitrates etc.)  Remove container lids and bungs slowly to release any internal pressure.  Isolate from sources of heat, naked flames or sparks.  Ensure fittings are earthed and flame proofed.  Ensure adequate ventilation.  Explosive air-vapour mixture may form.  Take precautions against static electricity and sparking.

Spill

Remove all ignition sources.  Isolate area.  Recover free liquid.  Absorb in dry inert material and place in sealable labelled drums.  Avoid breathing vapours.  Ventilate confined spaces or use breathing apparatus.  Keep out of sewers and drains by diking or impounding. Advise authorities.

Waste Disposal

Observe all Federal, State and Local regulations.  Dispatch sealed labelled material to approved waste authority.

| Fire / Explosion Hazard |  |
| --- | --- |
| Explosion Limit Upper: | 7.0% |
| Explosion Limit Lower: | 0.9% |
| Dust Explosion Hazard: | N/A |
| Hazardous Decomposition Products: | Smoke, Carbon monoxide |
| Hazardous Polymerisation Products/Reactions: | Unlikely |
| Extinguishing Media: | Foam, carbon dioxide, dry chemical. Cool drums with water spray |
| Other Precautions: | Fire fighter should wear self-contained breathing apparatus in fire situations. |

| Contact Points |  |
| --- | --- |
| South Coast Decorative Concrete Supplies: | (02) 44235 111 |
| Poisons Information Center: | 131 126 |
| Fire Brigade: | 000 |
| Ambulance: | 000 |
| Police: | 000 |

| Key to Abbreviations |
| --- |
| N/A | Not applicable |
| NAS | Not assigned |
| ºC | Degreed Celsius |
| k/Pa | Kilopascals |
| m/min |  |

We cannot anticipate all conditions under which this information and our products may be used. Users are advised to make their own tests to determine the safety and suitability of each product. All information in this Data Sheet is as up to date as possible. No warranty expressed or implied is made to the accuracy, reliability or completeness of this date. South Coast Decorative Concrete Supplies assumes no responsibility for personal injury or property damage to vendors, users or third parties caused by the material. Such vendors or users assume all risks associated with the use of the material.